## Slide 1: Lectrotab Retrofit Instructions (Replacing Bennett Standard System)
Standard Bennett Actuator (A1101A)
Standard Lectrotab Actuator (A-BK)
Old
New

## Slide 2
Removing Old Bennett Actuator
1) Remove the 3 upper mounting bracket screws (#14 x 1-1/2”).
2) Remove and dispose of the hydraulic tubing.
3) Remove the actuator by driving out the lower bracket pin. KEEP the lower bracket and pin. The Bennett pin and lower bracket will be used to mount the Lectrotab actuator.
4) Remove and dispose of the old Bennett actuator.

## Slide 3
Installing New Lectrotab Actuator
1) Innermost holes match the Bennett upper mounting bracket hole pattern. Punch or drill out innermost holes on Lectrotab upper mounting bracket.
2) Insert two conductor cable with vent tube through upper bracket center hole.
4) Next insert two conductor cable with vent tube through old Bennett hydraulic tube hole in transom.
5) Lastly, fill the upper bracket rear cavity, face, cable and transom holes with a 3M 5200 or similar sealant, and tighten upper bracket with screws (#14 x 1-1/2”) to transom.
Note:
A-BK actuator has 6’ (1.8m) cable and connects to 4 conductor interconnect cable (W4-cable length).
A-BK-13 actuator has 23’ (7m) cable length and
A-BK-24 actuator has 28’ (8.5m) cable length which connects directly to control switch.
3) Tighten upper bracket bolt snug against bracket so actuator rotates freely. Do not over-tighten.

## Slide 4
Installing New Lectrotab Actuator
6) Insert Lectrotab ram in existing Bennett lower bracket. Retrieve existing Bennett lower bracket pin and drive through bracket .
Actuator mounting is complete.
IMPORTANT: For tabs mounted under the hull bottom in a pocket, there must be a ¼” minimum gap clearance between the top surface of the tab plate and hull bottom (clearance is required to allow actuator ball screw to spin freely in fully retracted position). Spacers may be used under the actuator lower mounting bracket to provide the clearance gap. For vertical actuator applications, spacers may be required on the side or bottom of the actuator lower bracket for actuator and tab clearance.

## Slide 5
Installing New Lectrotab Control
Discard Bennett hydraulic pump, wiring and keypad control.
Choose a Lectrotab control from the following: a basic rocker switch (SAF-S), Oval control with LED trim tab indicators (SETR) or Wireless control with LED trim tab indicators (WTR).
Install the Lectrotab control of choice per the matching wiring diagram below.

## Slide 6
Installing Lectrotab Basic (SAF-S) Rocker Switch Control

## Slide 7
Installing Lectrotab Oval (SETR) Control

## Slide 8
Installing Lectrotab Wireless (WTR) Control